# Phys 481                                                                                           Winter 2012

# Worksheet # 6

Friday, January 27, 2012

# Name

Questions (5 pts):

In a diffraction experiment, a point source emitting light with the wavelength of 600 nm is used. The distance from the source to the diffracting aperture is 10 m, and the aperture is a hole of 1-mm diameter. Determine whether Fresnel or Fraunhofer diffraction applies when the screen-to-aperture distance is (a) 1 cm and (b) 2 m.