## Slide 1
Titrations
Analytical Chemistry!!
Titration requirements:
Quantitative chemical reaction
A measureable change at the equivalence point (visual?)
Perhaps a measureable quantity during the entire reaction
Commonly using a burette
Sometimes the titrant is generated in situ
Usually electrochemically
An experienced student with a burette and visual indicator can achieve <0.2% precision and accuracy
Slide 1

## Slide 2
If You’re Working in a Lab
with Enough Money ……..
Slide 2
https://www.metrohm.com/en-gb/products-overview/titration/titrotherm/titrotherm-automation/
Computer controlled syringe adds the titrant
Requires a continuously monitoring sensor technology

## Slide 3
Back to General Chemistry
General Classes of Titrations:
Acid/base
Precipitation
Redox (oxidation/reduction)
Complexation (ligands or chelating agents)
Did everyone run an acid/base titration in gen chem lab?
Let’s review weak acid chemistry:
HA + H2O H3O+ + A-
Kc = [A-][H3O+]
[HA][H2O]
Slide 3
Ka = [A-][H3O+]
[HA]

## Slide 4
Let’s Follow Where the Math Leads
Slide 4
Ka = [A-][H3O+]
[HA]
log(Ka) = log [A-][H3O+]
[HA]
log(Ka) = log([H3O+]) + log [A-]
[HA]
-log(Ka) = -log([H3O+]) - log [A-]
[HA]
pKa = pH - log [A-]
[HA]
pH = pKa + log [A-]
[HA]
The Henderson-Hasselbalch Equation
pH = -log([H3O+])

## Slide 5
Henderson-Hasselbalch Equation
Graph of pH vs Volume of Base
Slide 5
pH = pKa + log [A-]
[HA]
Chart: Titration of Benzoic Acid with NaOH
[A-] = [HA]  log (1/1) = 0  pH = pKa
[A-] = 10 x [HA]  log (10/1) = 1  pH = pKa +1
10 x [A-] = [HA]  log (1/10) = -1  pH = pKa -1
This is how we chose pH buffers

## Slide 6
Advanced Endpoint Detection
Or Calculus is Good for Something
Slide 6
Chart: Titration of Benzoic Acid with NaOH
 | A | B | C
1 | Vol | pH | ΔpH / Δvol
2 | 0.05 | 3.85 | 1st Derivative
3 | 0.1 | 3.92 | (B3-B2)/(A3-A2)
4 | 0.15 | 3.93 | (B4-B3)/(A4-A3)

## Slide 7
Advanced Endpoint Detection
Calculus is Good for Something Part 2
Slide 7
Chart: Titration of Benzoic Acid with NaOH
 | A | B | C | D
1 | Vol | pH | ΔpH / Δvol | Δ1st D / Δvol
2 | 0.05 | 3.85 | 1st Derivative | 
3 | 0.1 | 3.92 | (B3-B2)/(A3-A2) | 2st Derivative
4 | 0.15 | 3.93 | (B4-B3)/(A4-A3) | (C4-C3)/(A4-A3)

## Slide 8
Advanced Endpoint Detection
Requires Quality Data
Slide 8
Chart: Real Student Benzoic Acid Titration Data
Chart: Real Student Benzoic Acid Titration Data
Chart: Real Benzoic Acid Titration Data 1st Derivative
The 1st Law of Computers:
GIGO 
Garbage In Garbage Out
Experimental pH values only reported to 2 decimal places

## Slide 9
Colorimetric Endpoint Indicator Selection
Slide 9
pH indicators are weak acids whose acid/base conjugates are different colors
Change color at different pHs
Chart: Volume of base added (mL)
Chose your indicator so that it turns color in the pH range where your compound titration has it’s endpoint
 different pKas

## Slide 10
End Point vs Equivalence Point
Slide 10
Equivalence point:
Stoichiometry  amounts of sample and titrant are present
[Base titrant] = [Acid sample]
End Point:
When the detection system signals the end of the titration
[Base titrant] = [Acid sample] + [Detection reaction]
Use detection which doesn’t react with the titrant;
i.e. a pH electrode in an acid/base titration
Equivalence point = End point
The safest experimental approach?
Titrate a blank.
 A blank contains everything except the sample

## Slide 11
Non-aqueous or Mixed Solvent Titrations
Slide 11
Ka = [A-][H3O+]
[HA]
Will the measured pKa be too high or too low?
HA + H2O H3O+ + A-
Ions are less soluble in EtOH
Many of you will require some EtOH to dissolve your acid
What happens to acid/base equilibria when water’s not the solvent?
Kc= [A-][H3O+]
[HA][H2O]
Kc[H2O] =
Or not the only solvent?

## Slide 12
NaOH Solutions and CO2
Slide 12
2 OH- + CO2 H2O + CO32-
CO2 reacts with strong base OH-
to produce the weaker base CO32-
Since carbonate is a much weaker base than hydroxide, you can get titration curves that appear to have multiple endpoints
NaOH must be dissolved in carbonate free water
The lab preparators did that for you.
Please thank them - it’s a pain.
It’s up to you to minimize NaOH exposure to CO2 in the air while you do your titrations